## Slide 1: Introduction to MR
Robert Frost
Thanks for images/animations provided by Dylan Tisdall

## Slide 2: MRI signal from protons
Nuclei with odd number of protons/neutrons have ”spin” or angular momentum
“spin” + charge  magnetic moment
Bar magnets have magnetic moment
H1
+

## Slide 3
Lars Hanson, 2008

## Slide 5
Lars Hanson, 2008
“B0”, z direction
Net magnetisation M
“Precession”

## Slide 6: Precession
Property of something spinning (angular momentum) experiencing a force

## Slide 7: Proton precession
Frequency,
3T: ~128 MHz
7T: ~298 MHz
Radio frequencies (RF)

## Slide 8: Magnetic Resonance key points
Polarisation – net magnetisation M
Excitation – move away from z axis
Precession – M ar0und B0
Measure
Relaxation

## Slide 9: Excitation
Apply “RF pulse” to rotate magnetisation away from z
RF pulse has same frequency as the precession
Can change duration and magnitude of RF pulse to determine “flip angle”, e.g. 90 degrees
x
y
z

## Slide 10: Precession
A changing magnetic field in x-y plane  measure
William Overall

## Slide 11: Measure
A changing magnetic field
 Induces a voltage in coil of conducting wire

## Slide 12: Measure
A changing magnetic field in x-y plane
Signal strength

## Slide 13: Relaxation
Two independent components:
T2: decay of x-y component
  Measurable signal decays ~ <100 ms
T1: regrowth of z component
  Net Mz reforms ~ 1-5 sec

## Slide 14: Rotating frame
If we watch the precession of M while also spinning around the z axis at same frequency… then M appears still

## Slide 15: T2 relaxation
In rotating frame
1) spins experience inhomogeneous field (created by neighbours) 2) precess at different frequencies 3) spins “dephase”

## Slide 16: T2 relaxation
Net magnetisation (x-y component only)

## Slide 17: T1 & T2 relaxation
T2
T1

## Slide 18: Contrast
T1 regrowth of Mz
T2 decay of Mxy
T2 values:
WM = 75 ms
GM = 83 ms
T1 values:
WM = 850 ms
GM = 1550 ms

## Slide 19: Inversion Recovery
Excite here!

## Slide 20: Inversion recovery – T1 contrast

## Slide 21: Magnetic Resonance key points
Polarisation – net magnetisation M
Excitation – supply energy with RF pulse
Precession – M ar0und B0
Measure – changing magnetic field
Relaxation – decay of M in x-y, regrowth of M in z

## Slide 22: Spatial encoding
Field gradients

## Slide 23: Spatial encoding
Field gradients

## Slide 24: Magnetic Resonance Imaging
Polarisation
Excitation
Precession
Spatial encoding
Measure
Relaxation
Repeat, varying gradients
2D Inverse
Fourier Transform