## Slide 1: fMRI Analysis with the FreeSurfer Functional Analysis Stream (FS-FAST) Preprocessing, First Level Analysis, and Group Analysis

## Slide 2: Overview
<number>
Version 5.1 (April 2011)
Atlas Spaces
Directory Structure
Preprocessing
Setting up First-Level Analysis and Contrasts
Group Analysis
  Setting up
  Correction for multiple comparisons

## Slide 3
Time-series functional analysis
  Event-related, Blocked, Retinotopy, Functional Connectivity
Built on FreeSurfer
Surface-, Volume-, ROI-based
Group Analysis
Highly Automated
Command-line driven
Matlab/Octave and FSL used in the background
FSFAST

## Slide 4
Respect the inherent geometry of the brain structures (Smoothing and Clustering)
Cortex – 2D
Subcortical – 3D
Requires that analysis be done in three spaces:
  Left Hemisphere
  Right Hemisphere
  Subcortical Areas
Not simple volumetric-based for all voxels!
Philosophy

## Slide 5
<number>
FS-FAST Preprocessing
1B0 distortion correction not fully tested yet.
2Eventually will be done with CVS.
Atlas Spaces
MC
STC
Raw 3D+Time
Spatial
Normalization
+ B0 Correction1
3D+T MNI305
2D+T Left Hemi
2D+T Right Hemi
Masked 2D
Smoothing
Masked 2D
Smoothing
Masked 3D
Smoothing
12 DOF
Affine2
2D+Time
2D+Time
3D+Time

## Slide 6
<number>
FS-FAST Analysis
3D+T MNI305
2D +T Left Hemi
2D+T Right Hemi
First Level
GLM
First Level
GLM
First Level
GLM
X1, C1
Higher
Level GLM
Higher
Level GLM
Higher
Level GLM
XG, CG
2D Multiple
Comparisons
Correction
2D Multiple
Comparisons
Correction
3D Multiple
Comparisons
Correction
Final
Correction
Atlas Space
Masked, Smoothed

## Slide 7
<number>
Surface Masking
Remove medial wall
Intersect with functional brain mask
2D Smoothing only inside mask
Later individual subjects masks
merged (intersection).

## Slide 8
<number>
Volume (Subcortical) Masking
Anatomy
Mask
SubCor
Probability
(40 Subj)
Remove most of cortex
Remove some WM and CSF
Intersect with functional brain mask
3D Smoothing only inside mask
Later individual subjects masks merged (intersection).
Tip: use compressed NIFTI files (nii.gz)

## Slide 9
<number>
Correction for Multiple Comparisons
Cluster-based
Performed separately in each space
  2D clustering for Left and Right Hemispheres
  3D clustering for MNI305
  Cluster table for each individual space
Final cluster table is union of individual spaces
  IMPORTANT: p-values must be multiplied by x3 to correct for the three spaces

## Slide 10
Analyze anatomicals in FreeSurfer
Unpack each subject (dcmunpack,unpacksdcmdir)
Create subjectname file.
Copy paradigm files into run directories
Configure analyses (mkanalysis-sess, mkcontrast-sess)
Preprocess (preproc-sess)
First Level Analysis (selxavg3-sess)
Higher Level Analysis (isxconcat-sess, mri_glmfit )
Correction for Multiple Comparisons (mri_glmfit-sim)
FSFAST Pipeline Summary

## Slide 11
Project
Sess01
Sess02
Sess03
bold
003
005
006
f.nii (raw data)
FSFAST Directory Structure
bold
1. Project
2. Session
3. Functional
Subdirectory
(FSD, “bold”)
4. Run
5. Raw Time-
Series Data
Automation Requires Structure!

## Slide 12
Folder where all/most of your data reside (can use symbolic links to data too)
Directory where you will run most commands
NOT the same as $SUBJECTS_DIR
Project Directory
Project
Sess01
bold
003
f.nii (raw data)

## Slide 13
All the data collected between the time you put a subject into the scanner until you take him/her out.
  May include data across “breaks”
All one subject
Data from one subject may be spread over different sessions (eg, longitudinal study)
Session does not necessarily equal Subject
Folder name can be anything.
Session Directory
Project
Sess01
bold
003
f.nii (raw data)

## Slide 14
All the data associated with a given paradigm
Most people just have one paradigm and so only one FSD
Usually called “bold”
Default is “bold”
Functional Subdirectory (FSD, “bold”)
Project
Sess01
bold
003
f.nii (raw data)

## Slide 15
All the data collected between pressing the “Apply” button and the end of the scan.
Eg, 150 time points (TPs)
Raw functional data stored in this folder
Usually called “f.nii” or “f.nii.gz”
Raw data will be in “native functional space”, eg, 64x64x30, 3.125mm x 3.125mm x 6mm
Folder name will be 3-digit, zero-padded number, eg, “002”, “014”
Run Folder/Directory
Project
Sess01
bold
003
f.nii (raw data)

## Slide 16
Project
Sess01
Sess02
Sess03
bold
003
005
006
f.nii (raw data)
FSFAST Directory Structure
bold
1. Project
2. Session
3. Functional
Subdirectory
(FSD, “bold”)
4. Run
5. Raw Time-
Series Data
Automation Requires Structure!

## Slide 17
Unpack raw data from DICOM
Add paradigm files
Add subjectname file
Setting Up the Directory Structure
Things you need to do before running automated commands:

## Slide 18
unpacksdcmdir – Siemens only
dcmunpack – Siemens or GE (not sure about Philips)
Manually
1. Unpacking: Creating the Directory Structure from DICOM Files
Getting help:
dcmunpack -help
Get a summary of the scans in a DICOM directory
dcmunpack –src dicomdir -martinos
Unpack:
cd ProjectDir
dcmunpack –src dicomdir -martinos
–trg sess01
–run 3 bold nii f.nii
–run 5 bold nii f.nii
–run 6 bold nii f.nii
Sess01
bold
003
005
006
f.nii
f.nii
f.nii

## Slide 19
Codes Stimulus Schedule
Simple Text File
Manually copy into Run Folder
2. Add “Paradigm” File(s)
Sess01
bold
003
005
006
f.nii
odd.even.par
f.nii
odd.even.par
f.nii
odd.even.par
All have the same name
May have different content
Different codings have different names
odd.even.par

## Slide 20
Codes Stimulus Schedule (and Weight)
Four Columns
  Onset Time (Since Acq of 1st Saved Volume)
  Stimulus Code (0, 1, 2 ,3 …)
  Stimulus Duration
  Stimulus Weight (default is 1)
  Any other columns ignored
Simple Text File
Code 0 Always Fixation/NULL
Version 5 requires 4-column!
Paradigm File

## Slide 21
3. Add “subjectname” file
Integration with FreeSurfer anatomical analysis
Subject name is name passed to recon-all, eg,
  recon-all –all –subject bert
  $SUBJECTS_DIR/bert
Create a text file called “sess01/subjectname”, the content of the file will be, eg, “bert” (no quotes)
Sess01
bold
003
005
006
f.nii
odd.even.par
f.nii
odd.even.par
f.nii
odd.even.par
subjectname

## Slide 22
Project
Sess01
Sess02
Sess03
bold
003
005
006
FSFAST Directory Structure
bold
1. Project
2. Session
3. Functional
Subdirectory
(FSD, “bold”)
4. Run
5. Raw Time-
Series Data
f.nii
odd.even.par
f.nii
odd.even.par
f.nii
odd.even.par
subjectname
subjectname
bold
subjectname

## Slide 23
Congratulations: You are now ready to start running the “automated” commands … but before you do …

## Slide 24
<number>
Project
Sess01
Sess02
Sess03
Session Id File (“SessId”)
Text file with a list of sessions to process
Easy way to keep track of groups
Can have more than one
A good way to parallelize
FS-FAST Commands will often take a SessId file as input:
selxavg3-sess –sf sessid …
Will run for all sessions found in sessid
Alternatively, selxavg3-sess –s Sess01 –s Sess02 –s Sess03
sessid
Sess01
Sess02
Sess03

## Slide 25
OK, now you are ready to start running the “automated” commands …

## Slide 26
First-Level Analysis
Time-series analysis
Everything inside of a functional subdir (all runs)
Preprocessing
GLM Analysis
Sess01
bold
003
005
006
f.nii
odd.even.par
f.nii
odd.even.par
f.nii
odd.even.par
subjectname
Project

## Slide 27
Preprocessing
Registration Template Creation
Motion Correction
Slice-timing correction (if using)
Functional-Anatomical Registration
Mask creation
Intensity normalization, Part 1
Resampling raw time series to mni305, lh, and rh
Spatial smoothing
No automated B0 distortion correction yet

## Slide 28
Preprocessing Command
preproc-sess
–sf sessids
–surface fsaverage lhrh
–mni305
–fwhm 5
–per-run
Command Name
Session Id File
Surface-based (lh and rh of fsaverage)
Volume-based in mni305
Smoothing 5mm FWHM
Run-wise MC+registration
preproc-sess -help
Preprocess all runs of all sessions
Can take a long time!

## Slide 29
Directory Structure after Preprocessing
Final data in atlas space:
  fmcpr.sm5.fsaverage…
Lots of other intermediate files
Lots more boring details
bold
003
005
f.nii
odd.even.par
template.nii
template.log
fmcpr.nii
fmcpr.mcdat
mcprextreg
register.dof6.dat
global.meanval.dat
fmcpr.sm5.fsaverage.lh.nii
fmcpr.sm5.fsaverage.rh.nii
fmcpr.sm5.mni305.2mm.nii
Sess01
Project

## Slide 30
First Level GLM Analysis
Specify Task Model
  Event-related or Blocked
  AB-Blocked (Periodic two condition)
  Retinotopy
  Task timing (Paradigm file)
  Hemodynamic Response Function (HRF)
  Contrasts
Specify Nuisance and Noise Models
  Low frequency drifts
  Time point exclusion
  Motion Regressors
  Other (Physiology, RETROICOR)
  Temporal Whitening

## Slide 31: Example: Odd Even Blocks
<number>
y = X * 
Odd
Even
base
Data from
one voxel
Design Matrix
Regressors
=
Raw Time Series

## Slide 32
First Level GLM Analysis: Workflow
Do these two steps once regardless of number of sessions:
  Configure “Analysis” – collection of parameters, mkanalysis-sess
  Create Contrasts (mkcontrast-sess)
  Don’t even need data to do this
Do this for each session:
  Perform Analysis (selxavg3-sess)

## Slide 33
Configure First Level GLM Analysis
cd ProjectDir
mkanalysis-sess
-analysis oddeven.sm5.lh
-surface fsaverage lh
-fwhm 5
-paradigm oddeven.par
-event-related
-spmhrf 0
-refeventdur 4
-polyfit 2
-mcextreg
-nskip 4
-TR 2 -nconditions 2
Project
Sess01
Sess02

## Slide 34
Configuration: Analysis Name
mkanalysis-sess
-analysis oddeven.sm5.lh
-surface fsaverage lh
-fwhm 5
-paradigm oddeven.par
-event-related
-spmhrf 0
-refeventdur 4
-polyfit 2
-mcextreg
-nskip 4
-TR 2 -nconditions 2
Project
Sess01
Sess02
oddeven.sm5.lh
analysis.info
Analysis Name – name used to
reference this collection of parameters. Use a different name for a different set of parameters.

## Slide 35
Configuration: Preprocessing
mkanalysis-sess
-analysis oddeven.sm5.lh
-surface fsaverage lh
-fwhm 5
-paradigm oddeven.par
-event-related
-spmhrf 0
-refeventdur 4
-polyfit 2
-mcextreg
-nskip 4
-TR 2 -nconditions 2
Preprocessing options indicate what
the source time-series file name will be.
bold
003
005
fmcpr.sm5.fsaverage.lh.nii
fmcpr.sm5.fsaverage.rh.nii
fmcpr.sm5.mni305.2mm.nii

## Slide 36
Configuration: Preprocessing
mkanalysis-sess
-analysis oddeven.sm5.mni305
-mni305
-fwhm 5
-paradigm oddeven.par
-event-related
-spmhrf 0
-refeventdur 4
-polyfit 2
-mcextreg
-nskip 4
-TR 2 -nconditions 2
A different analysis is needed for each space (lh, rh, and mni305)
bold
003
005
fmcpr.sm5.fsaverage.lh.nii
fmcpr.sm5.fsaverage.rh.nii
fmcpr.sm5.mni305.2mm.nii
Project
oddeven.sm5.lh
oddeven.sm5.mni305

## Slide 37
Configuration: Stimulus Timing
mkanalysis-sess
-analysis oddeven.sm5.lh
-surface fsaverage lh
-fwhm 5
-paradigm oddeven.par
-event-related
-spmhrf 0
-refeventdur 4
-polyfit 2
-mcextreg
-nskip 4
-TR 2 -nconditions 2
bold
003
005
fmcpr.sm5.fsaverage.lh.nii
fmcpr.sm5.fsaverage.rh.nii
fmcpr.sm5.mni305.2mm.nii
oddeven.par

## Slide 38
Configuration: Task Type
mkanalysis-sess
-analysis oddeven.sm5.lh
-surface fsaverage lh
-fwhm 5
-paradigm oddeven.par
-event-related
-spmhrf 0
-refeventdur 4
-polyfit 2
-mcextreg
-nskip 4
-TR 2 -nconditions 2
Event-related and blocked are the same. Other possibilities are:
-abblocked
-retinotopy

## Slide 39
Configuration: HRF Model
mkanalysis-sess
-analysis oddeven.sm5.lh
-surface fsaverage lh
-fwhm 5
-paradigm oddeven.par
-event-related
-spmhrf 0
-refeventdur 4
-polyfit 2
-mcextreg
-nskip 4
-TR 2 -nconditions 2
Other options:
-fslhrf NDerivaties
-fir PreStim TotTimeWindow
-gammafit 2.25 1.25
SPM
FSL
FSFAST
SPM Canonical HRF
0 Derivatives

## Slide 40
Configuration: Reference Event Duration
mkanalysis-sess
-analysis oddeven.sm5.lh
-surface fsaverage lh
-fwhm 5
-paradigm oddeven.par
-event-related
-spmhrf 0
-refeventdur 4
-polyfit 2
-mcextreg
-nskip 4
-TR 2 -nconditions 2
Just set this to the duration of your event in seconds.

## Slide 41
Configuration: Nuisance Drift Modeling
mkanalysis-sess
-analysis oddeven.sm5.lh
-surface fsaverage lh
-fwhm 5
-paradigm oddeven.par
-event-related
-spmhrf 0
-refeventdur 4
-polyfit 2
-mcextreg
-nskip 4
-TR 2 -nconditions 2
2nd Order Polynomial. This is the default.
0: mean offset
1: temporal trend
2: quadratic trend
Can also specify a high-pass filter with
-hpf CutOffHz
where CutOffHz is the cut-off frequency in Hz (eg, .01). Careful with this.

## Slide 42
Configuration: Nuisance Motion
mkanalysis-sess
-analysis oddeven.sm5.lh
-surface fsaverage lh
-fwhm 5
-paradigm oddeven.par
-event-related
-spmhrf 0
-refeventdur 4
-polyfit 2
-mcextreg
-nskip 4
-TR 2 -nconditions 2
Use Motion Correction parameters as nuisance regressors. Can specify arbitrary regressor files with “–nuisreg file N”.
bold
003
005
f.nii
odd.even.par
template.nii
template.log
fmcpr.nii
fmcpr.mcdat
mcprextreg

## Slide 43
Configuration: Excluding Time Points
mkanalysis-sess
-analysis oddeven.sm5.lh
-surface fsaverage lh
-fwhm 5
-paradigm oddeven.par
-event-related
-spmhrf 0
-refeventdur 4
-polyfit 2
-mcextreg
-nskip 4
-TR 2 -nconditions 2
Skip the 1st 4 time points. Do not need to adjust stimulus timing. Alternative:
“-tpexclude tpexclude.dat” to remove any TP. Good for motion.
bold
003
005
f.nii
odd.even.par
template.nii
template.log
fmcpr.nii
fmcpr.mcdat
mcprextreg
tpexclude.dat

## Slide 44
Configuration: Why TR and NCond?
mkanalysis-sess
-analysis oddeven.sm5.lh
-surface fsaverage lh
-fwhm 5
-paradigm oddeven.par
-event-related
-spmhrf 0
-refeventdur 4
-polyfit 2
-mcextreg
-nskip 4
-TR 2 -nconditions 2
It could get this from the data and paradigm files, but this command is set up to run without the need of any data, so it needs to know the TR and number of conditions.
Number of conditions is the number of Non-Fixation/Non-NULL conditions.
2 = Odd + Even

## Slide 45: Contrasts: Odd Even Blocks
<number>
y = X * 
Odd
Even
base
Data from
one voxel
Design Matrix
Regressors
=
Raw Time Series
Two task conditions
One nuisance regressor
Need weight for each condition
Does the hemodynamic response amplitude to the Odd stimulus differ from that of Even?
 = 1*Odd -1* Even
C = [+1 -1] Contrast Matrix

## Slide 46
Configuration: Contrasts
Linear combination of regression coefficients (COPE, CON)
Weight for each condition
Embodies a hypothesis: Does the hemodynamic response amplitude to the Odd stimulus differ from that of Even?
C = [+1 -1]
mkcontrast-sess
-analysis oddeven.sm5.lh
-contrast odd-vs-even
-a 1
-c 2
paradigm file

## Slide 47
Configuration: Contrasts
-analysis as created by mkanalysis-sess
mkcontrast-sess
-analysis oddeven.sm5.lh
-contrast odd-vs-even
-a 1
-c 0
Project
Sess01
oddeven.sm5.lh
analysis.info
odd-vs-even.mat

## Slide 48
Configuration: Contrasts
-contrast ContrastName
name used to reference this contrast
unique within the given analysis
Creates ContrastName.mat (matlab)
mkcontrast-sess
-analysis oddeven.sm5.lh
-contrast odd-vs-even
-a 1
-c 0
Project
Sess01
oddeven.sm5.lh
analysis.info
odd-vs-even.mat

## Slide 49
Specifying Contrast Weights
“Active” – positive, “Control” – negative
Odd vs Even means Odd-Even
Paradigm File Encoding
mkcontrast-sess
-analysis oddeven.sm5.lh
-contrast odd-vs-even
-a 1
-c 2
paradigm file
Conditions with “–a” get +1
Conditions with “–c” get -1
Contrast Matrix C = [+1 -1]

## Slide 50
Odd vs Fixation
“Active” – positive, “Control” – implicit
Odd vs Fixation means Odd-Fixation
Do not need Fixation-Odd
Paradigm file coding
mkcontrast-sess
-analysis oddeven.sm5.lh
-contrast odd-vs-fix
-a 1
-c 0
paradigm file
Contrast Matrix C = [1 0]
Implicit contrast vs Fixation

## Slide 51
Configuration: Three Conditions
Happy
Sad
Mad
Hypothesis: response to Happy is different than the average response to Sad and Mad (Happy =? (Sad+Mad)/2)
mkcontrast-sess
-analysis faces.sm5.lh
-contrast happy-vs-sadmad
-a 1
-c 2
-c 3
C=[1 -0.5 -0.5]
Hypothesis: response to Happy is different than that to Mad
mkcontrast-sess
-analysis faces.sm5.lh
-contrast happy-vs-mad
-a 1
-c 3
Note: Condition 2 (Sad) not represented (set to 0)
C = [1 0 -1]

## Slide 52
Configuration: Summary
mkanalysis-sess, mkcontrast-sess
Need configuration for lh, rh, and mni305
Specify: Preproc, Task, Nuisance, Noise, Contrasts
Does not do analysis, just creates configuration
Do once for each parameter set (space)
Do once regardless of number of sessions
Should take a few seconds to run
Project
Sess01
oddeven.sm5.lh
analysis.info
odd-vs-fix.mat

## Slide 53
First-Level GLM Analysis
cd ProjectDir
selxavg3-sess –sf sessidfile –analysis oddeven.sm5.lh
Finds raw data, paradigm file, external regressors, etc
Constructs design and contrast matrices
Combines runs together using “smart” concatenation
(1st and 2nd level)
Performs GLM fit at each voxel
Tests contrasts at each voxel
All sessions specified in sessid file
May take a few hours, depending on how many sessions
Does not re-run if data are “up-to-date”
Will run preprocessing if not done already
Requires matlab or octave

## Slide 54
After First Level Analysis…
Project
Sess01
bold
oddeven.sm5.lh
odd-vs-even
ces.nii
cesvar.nii
sig.nii
1. Project
2. Session
3. Functional
Subdirectory
(FSD, “bold”)
4. Analysis Folder
5. Contrast Folder
6. Contrast Values
ces - contrast effect size,
COPE (FSL), CON (SPM)
cesvar - contrast variance
VARCOPE (FSL)
sig = -log10(p)

## Slide 55
First Level Analysis: Visualization
Surface-based analyses:
tksurfer-sess –s session –analysis oddeven.sm5.lh –c odd-vs-fix
tksurfer-sess –s session –a oddeven.sm5.rh –c odd-vs-fix
Volume-based analyses:
tkmedit-sess –s session –a oddeven.sm5.mni305 –c odd-vs-fix
One session at a time (-s session, NOT –sf sessidfile)
Can specify multiple contrasts, eg,
–c odd-vs-fix –c even-vs-fix –c odd-vs-even
Or all contrasts with “-call”
Note Shortcut: “-a” instead of “-analysis” and “-c instead of –contrast”

## Slide 56
First Level Analysis: Visualization
No activation in medial wall
No activation in cortex
Masking

## Slide 57
After First Level Analysis…
Project
Sess01
bold
oddeven.sm5.lh
odd-vs-even
ces.nii
cesvar.nii
Sess02
bold
oddeven.sm5.lh
odd-vs-even
ces.nii
cesvar.nii
Sess03
bold
oddeven.sm5.lh
odd-vs-even
ces.nii
cesvar.nii
…
1. Project
2. Session
3. Functional
Subdirectory
(FSD, “bold”)
4. Analysis Folder
5. Contrast Folder
6. Contrast Values

## Slide 58
<number>
FS-FAST Analysis
3D+T MNI305
2D +T Left Hemi
2D+T Right Hemi
First Level
GLM
First Level
GLM
First Level
GLM
X1, C1
Higher
Level GLM
Higher
Level GLM
Higher
Level GLM
XG, CG
2D Multiple
Comparisons
Correction
2D Multiple
Comparisons
Correction
3D Multiple
Comparisons
Correction
Final
Correction
Atlas Space
Masked, Smoothed

## Slide 59
Group/Higher Level Analysis: Consolidation
cd ProjectDir
isxconcat-sess
-analysis oddeven.sm5.lh
-contrast odd-vs-even
-sf group1.sessid
-o group1
Project
Sess01
bold
oddeven.sm5.lh
odd-vs-even
ces.nii
cesvar.nii
Sess02
bold
oddeven.sm5.lh
odd-vs-even
ces.nii
cesvar.nii
Sess03
bold
oddeven.sm5.lh
odd-vs-even
ces.nii
cesvar.nii
group1
oddeven.sm5.lh
odd-vs-even
ces.nii
cesvar.nii
isxconcat-sess -help
Like mris_preproc
in anatomical stream

## Slide 60
Project
Sess01
bold
oddeven.sm5.lh
odd-vs-even
ces.nii
Sess02
bold
oddeven.sm5.lh
odd-vs-even
ces.nii
Sess03
bold
oddeven.sm5.lh
odd-vs-even
ces.nii
group1
oddeven.sm5.lh
odd-vs-even
ces.nii
cesvar.nii
isxconcat-sess
-analysis oddeven.sm5.lh
-contrast odd-vs-even
-sf group1.sessid
-o group1
One frame/time point for each session
Order is IMPORTANT!!!
Order will be as listed in group1.sessid
Group/Higher Level Analysis: Consolidation

## Slide 61
Group/Higher Level Analysis
Project
group1
oddeven.sm5.lh
odd-vs-even
ces.nii
cesvar.nii
cd ProjectDir
cd group1/oddeven.sm5.lh/odd-vs-even
mri_glmfit
--surf fsaverage lh
--y ces.nii
--wls cesvar.nii
--fsgd group1.fsgd
--C group.con1.mtx
--C group.con2.mtx
--glmdir glm.group
See FreeSurfer Group Analysis, including correction for multiple comparisons.
http://surfer.nmr.mgh.harvard.edu/fswiki/FsTutorial/GroupAnalysis
mri_glmfit –help
glm.group

## Slide 62
Group/Higher Level Analysis
mri_glmfit
--surf fsaverage lh
--y ces.nii
--wls cesvar.nii
--fsgd group1.fsgd
--C group.con1.mtx
--C group.con2.mtx
--glmdir glm.group
Surface-based analysis on the left hemisphere of fsaverage.
For right hemisphere, use
“–surf fsaverage rh”.
For mni305, so not specify –surf.

## Slide 63
Group/Higher Level Analysis
mri_glmfit
--surf fsaverage lh
--y ces.nii
--wls cesvar.nii
--fsgd group1.fsgd
--C group.con1.mtx
--C group.con2.mtx
--glmdir glm.group
Lower-level contrast input data, one frame/time point for each subject.

## Slide 64
Group/Higher Level Analysis
mri_glmfit
--surf fsaverage lh
--y ces.nii
--wls cesvar.nii
--fsgd group1.fsgd
--C group.con1.mtx
--C group.con2.mtx
--glmdir glm.group
Lower-level contrast variances, one frame/time point for each subject.
Performs weighted least squares
(Pseudo-Mixed Effects)

## Slide 65
Group/Higher Level Analysis
mri_glmfit
--surf fsaverage lh
--y ces.nii
--wls cesvar.nii
--fsgd group1.fsgd
--C group.con1.mtx
--C group.con2.mtx
--glmdir glm.group
FSGD file must have same order
of sessions as sessidfile used
when running isxconcat-sess
isxconcat-sess
-analysis oddeven.sm5.lh
-contrast odd-vs-even
-sf group1.sessid
-o group1

## Slide 66
Group/Higher Level Analysis
mri_glmfit
--surf fsaverage lh
--y ces.nii
--wls cesvar.nii
--fsgd group1.fsgd
--C group.con1.mtx
--C group.con2.mtx
--glmdir glm.group
Higher Level/Group contrasts.
Eg, Normal vs Schizophrenia
Easily confused with lower level
contrasts (eg, odd-vs-even).
Project
group1
oddeven.sm5.lh
odd-vs-even
ces.nii
cesvar.nii
glm.group
group.con1
sig.nii
group.con2
sig.nii

## Slide 67
Surface-based Correction for Multiple Comparisons
Project
group1
oddeven.sm5.lh
odd-vs-even
ces.nii
cesvar.nii
cd ProjectDir
cd group1/oddeven.sm5.lh/odd-vs-even
mri_glmfit-sim
--glmdir glm.group
--cache pos 2
--cwpvalthresh .0166
glm.group
group.con1
sig.nii
2D Cluster-based Correction at p < .05
Masking

## Slide 68
Surface-based Correction for Multiple Comparisons
Project
group1
oddeven.sm5.lh
odd-vs-even
ces.nii
cesvar.nii
mri_glmfit-sim
--glmdir glm.group
--cache pos 2
--cwpvalthresh .0166
glm.group
group.con1
sig.nii
2D Cluster-based Correction at p < .05

## Slide 69
Surface-based Correction for Multiple Comparisons
mri_glmfit-sim
--glmdir glm.group
--cache pos 2
--cwpvalthresh .0166
2D Cluster-based Correction at p < .05
Use pre-cached simulation results
positive group contrast
voxelwise threshold = 2 (p<.01)
Can use another simulation or permutation

## Slide 70
Surface-based Correction for Multiple Comparisons
mri_glmfit-sim
--glmdir glm.group
--cache pos 2
--cwpvalthresh .0166
2D Cluster-based Correction at p < .05
Cluster-wise threshold p<.0166
Why Cluster-wise threshold p<.0166 when I wanted p < .05?
Correction across 3 spaces: lh, rh, and mni305: .0166 = .05/3
Bonferroni Correction

## Slide 71
Correction for Multiple Comparisons Output (Surface)
mri_glmfit-sim
--glmdir glm.group
--cwpvalthresh .0166
--cache pos 2
glm.group
group.con1
sig.nii
cache.th20.pos.sig.cluster.nii – map of significance of clusters
cache.th20.pos.sig.ocn.annot – annotation of significant clusters
cache.th20.pos.sig.cluster.summary – text file of cluster table (clusters, sizes, MNI305 XYZ, and their significances)
Only shows clusters p<.0166
Cluster significance values not corrected for 3 spaces!

## Slide 72
Project
group1
oddeven.sm5.lh
odd-vs-even
ces.nii
cesvar.nii
isxconcat-sess
-analysis oddeven.sm5.mni305
-contrast odd-vs-even
-sf group1.sessid
-o group1
oddeven.sm5.mni305
odd-vs-even
ces.nii
cesvar.nii
Group MNI305 Analysis
oddeven.sm5.rh
odd-vs-even
ces.nii
cesvar.nii

## Slide 73
Group MNI305 Analysis
mri_glmfit
--y ces.nii
--wls cesvar.nii
--fsgd group1.fsgd
--C group.con1.mtx
--C group.con2.mtx
--glmdir glm.group
Command-line is very similar to surface
No “–surf fsaverage lh”
Surface-base command
mri_glmfit
--surf fsaverage lh
--y ces.nii
--wls cesvar.nii
--fsgd group1.fsgd
--C group.con1.mtx
--C group.con2.mtx
--glmdir glm.group

## Slide 74
Volume-based Correction for Multiple Comparisons
Project
group1
oddeven.sm5.mni305
odd-vs-even
ces.nii
cesvar.nii
cd ProjectDir
cd group1/oddeven.sm5.mni305/odd-vs-even
mri_glmfit-sim
--glmdir glm.group
--grf pos 2
--cwpvalthresh .0166
glm.group
group.con1
sig.nii
3D Cluster-based Correction at p < .05
Masking

## Slide 75
Volume-based Correction for Multiple Comparisons
Project
group1
oddeven.sm5.mni305
odd-vs-even
ces.nii
cesvar.nii
mri_glmfit-sim
--glmdir glm.group
--grf pos 2
--cwpvalthresh .0166
glm.group
group.con1
sig.nii
3D Cluster-based Correction at p < .05

## Slide 76
Volume-based Correction for Multiple Comparisons
mri_glmfit-sim
--glmdir glm.group
--grf pos 2
--cwpvalthresh .0166
3D Cluster-based Correction at p < .05
Use Gaussian Random Field
positive group contrast
voxelwise threshold = 2 (p<.01)
Can use simulation or permutation

## Slide 77
Volume-based Correction for Multiple Comparisons
mri_glmfit-sim
--glmdir glm.group
--grf pos 2
--cwpvalthresh .0166
3D Cluster-based Correction at p < .05
Cluster-wise threshold p<.0166
Why Cluster-wise threshold p<.0166 when I wanted p < .05?
Correction across 3 spaces: lh, rh, and mni305: .0166 = .05/3
Bonferroni Correction

## Slide 78
Correction for Multiple Comparisons Output (Volume)
mri_glmfit-sim
--glmdir glm.group
--cwpvalthresh .0166
--grf pos 2
glm.group
group.con1
sig.nii
grf.th2.pos.sig.cluster.nii – map of significance of clusters
grf.th2.pos.sig.ocn.nii – segmentation of significant clusters
grf.th2.pos.sig.cluster.summary – text file of cluster table (clusters, sizes, MNI305 XYZ, and their significances)
Only shows clusters p<.0166
Cluster significance values not corrected for 3 spaces!

## Slide 79
Project
group1
oddeven.sm5.lh
odd-vs-even
ces.nii
Full Group Analysis
oddeven.sm5.mni305
odd-vs-even
ces.nii
oddeven.sm5.rh
odd-vs-even
ces.nii
glm.group
glm.group
glm.group
Sess01
bold
oddeven.sm5.lh
odd-vs-even
ces.nii
cesvar.nii
sig.nii
003
f.nii (raw data)
oddeven.par
subjectname

## Slide 80
Analyze anatomicals in FreeSurfer
Unpack each subject (dcmunpack,unpacksdcmdir)
Create subjectname file.
Copy paradigm files into run directories
Configure analyses (mkanalysis-sess, mkcontrast-sess)
Preprocess (preproc-sess)
First Level Analysis (selxavg3-sess)
Higher Level Analysis (isxconcat-sess, mri_glmfit )
Correction for Multiple Comparisons (mri_glmfit-sim)
Publish (publish-sess )
FSFAST Pipeline Summary

## Slide 81
<number>