## Slide 1: Introduction to diffusion MRI
Anastasia Yendiki
HMS/MGH/MIT Athinoula A. Martinos Center for Biomedical Imaging

## Slide 2: White-matter imaging
Axons measure ~m in width
They group together in bundles that traverse the white matter
We cannot image individual axons but we can image bundles with diffusion MRI
Useful in studying neurodegenerative diseases, stroke, aging, development…
From Gray's Anatomy: IX. Neurology
From the National Institute on Aging

## Slide 3: Diffusion in brain tissue
Gray matter: Diffusion is unrestricted  isotropic
White matter: Diffusion is restricted  anisotropic
Differentiate between tissues based on the diffusion (random motion) of water molecules within them

## Slide 4: Diffusion MRI
Magnetic resonance imaging can provide “diffusion encoding”
Magnetic field strength is varied by gradients in different directions
Image intensity is attenuated depending on water diffusion in each direction
Compare with baseline images to infer on diffusion process
No diffusion encoding
Diffusion encoding in direction g1
g2
g3
g4
g5
g6

## Slide 5: How to represent diffusion
At every voxel we want to know:
  Is this in white matter?
  If yes, what pathway(s) is it part of?
    What is the orientation of diffusion?
    What is the magnitude of diffusion?
A grayscale image cannot capture all this!

## Slide 6: Tensors
One way to express the notion of direction is a tensor D
A tensor is a 3x3 symmetric, positive-definite matrix:
D is symmetric 3x3  It has 6 unique elements
Suffices to estimate the upper (lower) triangular part
d11 d12 d13
d12 d22 d23
d13 d23 d33
D =

## Slide 7: Eigenvalues & eigenvectors
The matrix D is positive-definite 
  It has 3 real, positive eigenvalues 1, 2, 3 > 0.
  It has 3 orthogonal eigenvectors e1, e2, e3.
D = 1 e1 e1´ + 2 e2 e2´ + 3 e3 e3´
eigenvalue
eix
eiy
eiz
ei =
eigenvector
1 e1
2 e2
3 e3

## Slide 8: Physical interpretation
Eigenvectors express diffusion direction
Eigenvalues express diffusion magnitude
1 e1
2 e2
3 e3
1 e1
2 e2
3 e3
Isotropic diffusion:
1  2  3
  Anisotropic diffusion:
  1 >> 2  3
One such ellipsoid at each voxel: Likelihood of water molecule displacements at that voxel

## Slide 9: Diffusion tensor imaging (DTI)
Direction of eigenvector corresponding to greatest eigenvalue
Image:
An intensity value at each voxel
Tensor map:
A tensor at each voxel

## Slide 10: Diffusion tensor imaging (DTI)
Image:
An intensity value at each voxel
Tensor map:
A tensor at each voxel
Direction of eigenvector corresponding to greatest eigenvalue
Red: L-R, Green: A-P, Blue: I-S

## Slide 11: Summary measures
Mean diffusivity (MD):
Mean of the 3 eigenvalues
Fractional anisotropy (FA): Variance of the 3 eigenvalues, normalized so that 0 (FA) 1
Faster
diffusion
Slower
diffusion
Anisotropic
diffusion
Isotropic
diffusion
MD(j) = [1(j)+2(j)+3(j)]/3
[1(j)-MD(j)]2 + [2(j)-MD(j)]2 + [3(j)-MD(j)]2
FA(j)2 =
1(j)2 + 2(j)2 + 3(j)2
3
2

## Slide 12: More summary measures
Axial diffusivity: Greatest of the 3 eigenvalues
Radial diffusivity: Average of 2 lesser eigenvalues
Inter-voxel coherence: Average angle b/w the major eigenvector at some voxel and the major eigenvector at the voxels around it
AD(j) = 1(j)
RD(j) = [2(j) + 3(j)]/2

## Slide 13: Beyond the tensor
High angular resolution diffusion imaging (HARDI): More complex models to capture more complex microarchitecture
  Mixture of tensors [Tuch’02]
  Higher-rank tensor [Frank’02, Özarslan’03]
  Ball-and-stick [Behrens’03]
  Orientation distribution function [Tuch’04]
  Diffusion spectrum [Wedeen’05]
The tensor is an imperfect model: What if more than one major diffusion direction in the same voxel?

## Slide 14: Models of diffusion
Diffusion spectrum (DSI): Full distribution of orientation and magnitude
Orientation distribution function (Q-ball): No magnitude info, only orientation
Ball-and-stick: Orientation and magnitude for up to N anisotropic compartments
Tensor (DTI): Single orientation and magnitude

## Slide 15: Example: DTI vs. DSI
From Wedeen et al., Mapping complex tissue architecture with diffusion spectrum magnetic resonance imaging, MRM 2005

## Slide 16: Data acquisition
Remember: A tensor has six unique parameters
d11
d13
d12
d22
d23
d33
To estimate six parameters at each voxel, must acquire at least six diffusion-weighted images
HARDI models have more parameters per voxel, so more images must be acquired
d11 d12 d13
d12 d22 d23
d13 d23 d33
D =

## Slide 17: Choice 1: Gradient directions
True diffusion direction || Applied gradient direction
 Maximum attenuation
True diffusion direction  Applied gradient direction
 No attenuation
To capture all diffusion directions well, gradient directions should cover 3D space uniformly
Diffusion-encoding gradient g
Displacement detected
Diffusion-encoding gradient g
Displacement not detected
Diffusion-encoding gradient g
Displacement partly detected

## Slide 18: How many directions?
Acquiring data with more gradient directions leads to:
  More reliable estimation of diffusion measures
  Increased imaging time  Subject discomfort, more susceptible to artifacts due to motion, respiration, etc.
DTI:
  Six directions is the minimum
  Usually a few 10’s of directions
  Diminishing returns after a certain number [Jones, 2004]
HARDI/DSI:
  Usually a few 100’s of directions

## Slide 19: Choice 2: The b-value
The b-value depends on acquisition parameters:
b = 2 G2 2 ( - /3)
   the gyromagnetic ratio
  G the strength of the diffusion-encoding gradient
   the duration of each diffusion-encoding pulse
   the interval b/w diffusion-encoding pulses
90
180
acquisition
G



## Slide 20: How high b-value?
Increasing the b-value leads to:
  Increased contrast b/w areas of higher and lower diffusivity in principle
  Decreased signal-to-noise ratio  Less reliable estimation of diffusion measures in practice
DTI: b ~ 1000 sec/mm2
HARDI/DSI: b ~ 10,000 sec/mm2
Data can be acquired at multiple b-values for trade-off
Repeat acquisition and average to increase signal-to-noise ratio

## Slide 21: Looking at the data
A diffusion data set consists of:
A set of non-diffusion-weighted a.k.a “baseline” a.k.a. “low-b” images (b-value = 0)
A set of diffusion-weighted (DW) images acquired with different gradient directions g1, g2, … and b-value >0
The diffusion-weighted images have lower intensity values
Baseline
image
Diffusion-weighted
images
b2, g2
b3, g3
b1, g1
b=0
b4, g4
b5, g5
b6, g6

## Slide 22: Distortions: Field inhomogeneities
Causes:
  Scanner-dependent (imperfections of main magnetic field)
  Subject-dependent (changes in magnetic susceptibility in tissue/air interfaces)
Results:
  Signal loss in interface areas
  Geometric distortions (warping) of the entire image
Signal loss

## Slide 23: Distortions: Eddy currents
Cause: Fast switching of diffusion-encoding gradients induces eddy currents in conducting components
Eddy currents lead to residual gradients that shift the diffusion gradients
The shifts are direction-dependent, i.e., different for each DW image
Result: Geometric distortions
From Le Bihan et al., Artifacts and pitfalls in diffusion MRI, JMRI 2006

## Slide 24: Data analysis steps
Pre-process images to reduce distortions
  Either register distorted DW images to an undistorted (non-DW) image
  Or use information on distortions from separate scans (field map, residual gradients)
Fit a diffusion model at every voxel
  DTI, DSI, Q-ball, …
Do tractography to reconstruct pathways and/or
Compute measures of anisotropy/diffusivity and compare them between populations
  Voxel-based, ROI-based, or tract-based statistical analysis